## Slide 1: CURRENT PRACTICES: MANAGEMENT OF CENTRAL LINES
IN THE OUTPATIENT SETTING

## Slide 2: WHAT IS A CENTRAL CATHETER?
CVAD—CENTRAL VENOUS ACCESS DEVICE
THE TIP ENDS UP IN THE SUPERIOR VENA CAVA

## Slide 3: CVAD PROS:
RAPID HEMODILUTION OF INFUSATE
CAUSES LESS VENOUS IRRITATION
CAN BE USED FOR LONG PERIODS OF TIME

## Slide 4: CVAD CONS:
RISK OF THROMBOSIS
RISK OF INFECTION

## Slide 5: CVADS APPROPRIATE FOR THE OUTPATIENT SETTING
PICC’s
TUNNELED CATHETERS
  GROSHONG
  HICKMAN
SUB-Q PORTS (IF FREQUENT ACCESS IS NOT REQUIRED)
  MEDIPORT
  PORTACATH

## Slide 6: CVADS NOT APPROPRIATE FOR THE OUTPATIENT SETTING
JUGULAR VEIN CATHS
PERCUTANEOUSLY PLACED SUBCLAVIAN CATHS
PERCUTANEOUSLY PLACED FEMORAL CATHS

## Slide 7: WHY?
RESEARCH!
  PERCUTANEOUSLY CVADS HAVE INCREASED INFECTION RATES WHEN COMPARED TO TUNNELED CATHS
    (HIV CLIENTS TREATED WITH FOSCARNET/GLANCICLOVIR FOR CMV)
  ALL CVADS SHOULD BE SINGLE-LUMEN (IN OUTPATIENT SETTING)
  IF MULTI-LUMEN
    ONE LUMEN SHOULD BE DEDICATED TO TPN ONLY
    LABEL IT!
    NO: BLOOD, FLUIDS, MEDS, ETC. SHOULD BE INFUSED OR DRAWN FROM THE TPN-DEDICATED PORT

## Slide 8: WHO QUALIFIES FOR OUTPATIENT CVAD THERAPY?
1. MUST BE CLINICALLY STABLE
  DECREASES RISK OF SUDDEN, LIFE-THREATENING CHANGE IN MEDICAL STATUS
2. MUST HAVE AN ADEQUATE HOME ENVIRONMENT FOR INFUSION THERAPY
3. MUST BE ABLE TO SELF-ADMINISTER INFUSION THERAPY (OR HAVE CARETAKER AVAILABLE TO ADMINISTER)
4. SHOULD (IDEALLY) LIVE WITH SOMEONE WHO CAN RECOGNIZE ADVERSE THERAPY EFFECTS
  SOME SIDE EFFECTS ARE LIFE-THREATENING
5. SHOULD BE WILLING AND ABLE TO DEAL WITH NECESSARY ROUTINES ASSOCIATED WITH OUTPATIENT INFUSION THERAPY
  VERY IMPORTANT IF PATIENT HAS HISTORY OF ILLICIT DRUG OR ETOH ABUSE, DEMENTIA, CULTURAL CONFLICTS WITH THERAPY OR UNWILLINGNESS TO ADHERE TO THERAPEUTIC REGIMEN

## Slide 9
6. MUST HAVE RELIABLE TRANSPORTATION
  COMPLEX INFUSION THERAPY AT AN INFUSION CENTER OR AT HOME
  SOME TREATMENTS HAVE SIGNIFICANT ADVERSE EFFECTS
  TAXI-VOUCHER SYSTEM AT UC/SAN FRANCISCO HOSPITAL FOR EXAMPLE, IF RECEIVING A POTENTIALLY TOXIC THERAPY

## Slide 10: OTHER CONSIDERATIONS…
SELECTION OF THE CORRECT DEVICE DEPENDS ON PURPOSE AND IMPACT ON QUALITY OF LIFE
PATIENT PREFERENCE
REPEATED NEEDLESTICKS OKAY?
WANT TO SWIM OR BATHE?
VISUAL ACUITY OK?
PERIPHERAL VENOUS ACCESS GOOD?

## Slide 11: TYPES OF CVADS
FOR OUTPATIENT THERAPY

## Slide 12: PICC LINES
PERIPHERALLY INSERTED CENTRAL CATHETERS
INSERTED IN CEPHALIC OR BASILIC VEIN IN THE ANTECUBITAL FOSSA
THREADED ALL THE WAY INTO THE SUPERIOR VENA CAVA
BEST FOR CLIENTS WHO REQUIRE DAILY INFUSION THERAPY FOR UP TO 6 MONTHS
NO MAXIMUM DWELL TIME HAS BEEN ESTABLISHED

## Slide 13: WHO IS NOT SUITABLE FOR A PICC LINE?
CLIENTS WITH TRAUMATIZED ANTECUBITAL SPACES
HISTORY OF MULTIPLE FAILED CANNULATION ATTEMPTS
VERY ACTIVE CLIENTS
  RISK OF DISLODGEMENT
  UPPER EXTREMITY MOVEMENT MAY BE LIMITED

## Slide 14: DISADVANTAGES OF PICC LINES
RESTRICTED FLOW RATE (SMALL LUMEN)
NEED FOR INTACT VENOUS ANATOMY IN THE ARMS FOR PLACEMENT
INCREASED RISK OF VENOUS THROMBOSIS IN THE EXTREMITY USED
NEED FOR SUTURES TO PREVENT ACCIDENTAL DISLODGEMENT

## Slide 15: PICC LINES…
CAN BE INSERTED BY CERTIFIED NURSES OR HEALTH CARE PROVIDERS
  IN RADIOLOGY
  IN MD’S OFFICE
  IN PATIENT’S HOME
XRAY IS REQUIRED TO CONFIRM TIP PLACEMENT
CATHETERS ARE THIN-WALLED AND CAN BURST
  FROM HIGH FLOW RATES
  FROM EXCESSIVE PRESSURE WHEN FLUSHING
VACUUM BLOOD-COLLECTION SYSTEM
  USE 10 ML SYRINGE TO COLLECT BLOOD SPECIMENS

## Slide 16: DID YOU KNOW?
IT IS NOT UNCOMMON FOR PATIENTS TO HAVE PHLEBITIS WITHIN THE FIRST 10 DAYS OF INSERTION?
  REDNESS WILL EXTEND FROM INSERTION SITE TO SEVERAL INCHES ABOVE IT
  ELEVATE ARM
  APPLY WARM COMPRESSES
  ASSESS FOR CELLULITIS

## Slide 17: PICC LINE CARE
ASSESS EXTERNAL CATHETER
  LEAKAGE
  HUB COMMECTION FOR CRACKING
ADMIN SETS/SECONDARY SETS/ADD-ON’s SHOULD BE REPLACED EVERY 72 HOURS
BLOOD SETS/BLOOD PRODUCTS/HYPERALIMENTATION/LIPID EMULSION TUBINGS SHOULD BE REPLACED EVERY 24 HOURS
ASSESS SUTURE PLACEMENT
  IF SUTURES MISSING, SECURE UNTIL THEY CAN BE REPLACED

## Slide 18: WITH EACH PICC DRESSING CHANGE…
MEASURE EXTERNAL CATH LENGTH AND DOCUMENT
IF EXTERNAL CATH GETS LONGER, MUST HAVE XRAY FOR CHECKING PLACEMENT OF CATH TIP
PROPER FLUSHING CAN HELP PREVENT THROMBOSIS
SASH (SALINE-ADMINISTER DRUG-SALINE-HEPARIN) PROTOCOL
FREQUENCY OF FLUSHING IDLE PICC LINES:
  VARIES FROM 8 HOURS TO WEEKLY

## Slide 19: S-A-S-H
S—SALINE
A—ADMINISTER DRUG
S—SALINE
H—HEPARIN

## Slide 20: TUNNELED CENTRAL VENOUS CATHETERS
LONG-TERM EXTERNAL CATHETERS
MADE FROM DURABLE, MEDICAL-GRADE SILICONE
“TUNNELED” SUBCUTANEOUSLY BETWEEN VEIN INSERTION SITE AND EXIT SITE
TIP OF CATH IN SUPERIOR VENA CAVA
DACRON CUFF ATTACHED JUST ABOVE EXIT SITE
7-10 DAYS AFTER INSERTION, SCAR TISSUE GROWS ONTO THE CUFF
  ANCHORS
  PREVENTS INFECTION

## Slide 21: TUNNELED CVADS
INSERTED IN
  SURGICAL SUITE
  INTERVENTIONAL RADIOLOGIC SUITE
EXIT SITE MUST BE DRESSED UNTIL IT HEALS
  STERILE GAUZE
  TRANSPARENT DRESSING
PREVENT DISLODGEMENT FOR 2-4 WEEKS
CONTINUE TO SECURE TO PREVENT ENTANGLEMENT AND PULLING ON CUFF
WASH WITH SOAP AND WATER
ASSESS DAILY FOR INFECTION
SASH

## Slide 22: IMPLANTED PORTS
SELF-SEALING SILICONE ENCASED IN TITANIUM OR PLASTIC HOUSING THAT IS ATTACHED TO A SILICONE CATHETER
PORT COMPLETELY UNDER THE SKIN—NO EXTERNAL PARTS
BEST FOR CYCLIC THERAPIES
BEST FOR PATIENTS WHO DON’T WANT EXTERNAL PARTS TO CARE FOR
HUBER NEEDLE IS NEEDED TO ACCESS PORT
TRADITIONAL NEEDLE WOULD LACERATE THE PORT SEPTUM
  RESULTS IN BLOOD LEAKAGE
  CONTACT WITH AIR

## Slide 23: IMPLANTED PORTS…
DESIGNED FOR 500-2000 “STICKS”
PLACED IN CHEST OR ARM
  CHEST PORT
  PASport
LOWER INFECTION RATES REPORTED
DON’T NEED ROUTINE FLUSHING
BEST FOR INTERMITTENT THERAPY

## Slide 24: DID YOU KNOW?
DAILY ACCESSING OF IMPLANTED PORTS CAN CAUSE SKIN BREAKDOWN AT THE SITE?
SKIN IRRITATION CAN LEAD TO PORT INFECTION
SURGERY IS REQUIRED TO REMOVE AND INSPECT PORT (WHEN INFECTION IS SUSPECTED)
THEREFORE, INFECTION IS MORE COSTLY AND DIFFICULT TO TREAT WITH PORTS

## Slide 25: AFTER PORT PLACEMENT…
SLIGHT EDEMA AND TENDERNESS IS EXPECTED
ACCESS MAY BE DIFFICULT DUE TO EDEMA AND TENDERNESS
IF PORT IS NEEDED IMMEDIATELY, NEEDLE USED IN SURGERY IS LEFT IN UNTIL PORT CAN BE ACCESSED THROUGH THE SKIN
JUST LIKE PICC LINES, THE PASport (TRADE NAME OF AN IN THE ARM PORT) MAY CAUSE PHLEBITIS FOR THE FIRST 10 DAYS OR SO
ASSESS FOR CELLULITIS

## Slide 26: IMPLANTED PORTS…
USE ONLY HUBER NEEDLES
AVOID NEEDLES GREATER THAN 19 GAUGE
ANCHOR NEEDLE IN PORT WITH DRESSING, TAPE
CHECK PLACEMENT BY ASPIRATING BLOOD AND GIVING A SLOW FLUSH OF 5ML NS
NEVER FORCE

## Slide 27: GENERAL CARE OF CVADS
IN THE OUTPATIENT SETTING

## Slide 28
PROPER CARE SINGLE MOST IMPORTANT FACTOR
  REDUCES RISK OF COMPLICATIONS
AT HOME CLIENTS NEED FREQUENT ASSESSMENT OF CARE TECHNIQUE AND CARE SUPPLIES
NO SPECIFIC GUIDELINES EXIST BUT…
  USE STRICT ASEPTIC TECHNIQUE WHEN ACCESSING DEVICE
  MINIMMIZE CATHETER MANIPULATION DURING ENTRY INTO SYSTEM
  PROMPT DRESSING CHANGES IF WET, LOOSE, SOILED
  ROUTINE FLUSHING OF LINE WHEN NOT IN USE
  REMOVAL OF CATHETERS WHEN NO LONGER NEEDED

## Slide 29: EXIT-SITE CARE AND DRESSINGS
SKIN CLEANSING
  ALCOHOL + POVIDONE IODINE
  CHLORHEXIDINE**(2% WORKS BEST)
OINTMENTS HAVE NOT DEMONSTRATED EFFECTIVENESS IN PREVENTING INFECTION AT SITE
  CDC RECOMMENDS CHECKING MANUFACTURER’S RECOMMENDATIONS REGARDING COMPATIBILITY

## Slide 30: EXIT SITE CARE AND DRESSINGS
OCCLUSIVE DRESSINGS
  RESEARCH IS MIXED ON EFFECTIVENESS
TRANSPARENT DRESSINGS SHOULD:
  HAVE HIGH WATER PERMEABILITY
  KEEPS SITE DRY
  ASSESS SKIN INTEGRITY
  SWEATING
  SENSITIVITY
  DRESSING SHOULD BE INDIVIDUALIZED TO PATIENT
  CDC HAS NO RECOMMENDATIONS BUT…
    GAUZE MAY BE BETTER FOR BLEEDING OR OOZING SITE
  ASSESS FOR REDNESS, SWELLING, TENDERNESS, DRAINAGE

## Slide 31: FLUSHING CVADS
ALL REQUIRE ROUTINE FLUSHING WHEN NOT IN USE
  MAINTAIN PATENCY
  MINIMIZE THROMBOTIC COMPLICATIONS
FREQUENCY VARIES WITH DEVICE TYPE
NS GENERALLY RECOMMENDED
CONCENTRATION OF HEPARIN DIFFERS WITH DEVICE USED AND PATIENT’S CONDITION
GENERALLY, LOWEST EFFECTIVE CONCENTRATION OF HEPARIN SHOULD BE USED
VOLUME OF HEPARINIZED SALINE SHOULD BE ROUGHLY TWICE VOLUME OF CANNULA

## Slide 32: FLUSHING CVADS
SOME CVADS HAVE 2-WAY VALVES
PREVENT BLOOD BACK-UP INTO CATH
GROSHONG CATHETERS, FOR EXAMPLE
MAY BE FLUSHED WEEKLY WITH NS ONLY

## Slide 33: FLUSHING CVADS
MEDS MAY NOT BE COMPATIBLE WITH HEPARIN
  MUST FLUSH BEFORE AND AFTER EACH DIFFERENT MED WITH SALINE
  FLUSH WITH HEPARIN AFTER LAST SALINE FLUSH
IF DRAWING BLOOD FROM A DEVICE
  DISCARD FIRST 5-10 ML OF BLOOD

## Slide 34: CVAD COMPLICATIONS

## Slide 35: PERI-PROCEDURAL
PNEUMOTHORAX
HEMATOMA
AIR EMBOLISM
CARDIAC ARRHYTHMIA
ARTERIAL PUNCTURE
PLEXUS IRRITATION
PERFORATION OF HEART AND GREAT VESSELS

## Slide 36: POST-INSERTION
PHLEBITIS
INFECTION**
SEPTICEMIA
SVC SYNDROME
  OCCLUSION OF SUPERIOR VENA CAVA
VENOUS THROMBOSIS**
TORSION OF THE PORT RESERVOIR
CATHETER FRACTURE OR EMBOLISM
PINCH-OFF SYNDROME FOR TUNNELED CATHETERS
  CATH COMPRESSED BETWEEN FIRST RIB AND CLAVICLE
**MOST COMMON COMPLICATIONS

## Slide 37: OTHER COMPLICATIONS
CATHETER MIGRATION
  RARE
CATHETER FRACTURE SIGNS AND SYMPTOMS:
  CHEST WALL SWELLING AT INSERTION SITE
  PAIN IN THE SHOULDER OR PORT AREA WITHOUT SWELLING
  RESISTANCE TO INJECTION OR WITHDRAWAL OF FLUIDS
  SUDDEN ONSET OF CHEST PAIN OR COUGH
REPAIR KITS FOR BROKEN HUBS AND EXTERNAL TUBING

## Slide 38: OTHER COMPLICATIONS
EXTRAVASATION
CAUSED BY:
  NEEDLE DISLODGMENT
  DAMAGE TO CATHETER
  FIBRIN AND THROMBUS FORMATION
  CAUSES OCCLUSION AND LEAKAGE
ASSESS CATH FUNCTION BEFORE ADMINISTERING CHEMO
ASSESS SITE FOR:
  REDNESS
  SWELLING
  TENDERNESS
  PT COMPLAINTS DURING INFUSION

## Slide 39: CVAD THROMBOSIS
CAUSES
  PLATELET DEPOSITION ON FOREIGN SUBSTANCES
  FIBRIN SHEATHS (5-7 DAYS)
  CATHETER TIP PLACEMENT DIFFICULTIES
  VENOUS IRRITATION
    FROM CHEMOTHERAPY
    HIGH OSMOLARITY SOLUTIONS
    DRUG PRECIPATION WITHIN CATHETER
  VENOUS STASIS FROM TUMOR COMPLRESSION

## Slide 40: CVAD THROMBOSIS SYMPTOMS
DIFFICULTY IN ASPIRATING FROM THE CATH
MAY HAVE NO SYMPTOMS IN EARLY STAGES
SHOULDER OR ARM PAIN
UNILATERAL SWELLING OF ARM, NECK, OR FACE
CYANOSIS
VENOUS DISTENTION OR PALPABLE VENOUS CORD
PROMINENT SUPERFICIAL VEINS
SVC CYNDROME OR PULMONARY EMBOLUS

## Slide 41: CVAD THROMBOSIS DIAGNOSIS/TREATMENT
CONFIRMED WITH:
  X RAY STUDIES (WITH CONTRAST)
  ULTRASOUND
  CT SCANNING
TREATMENT INCLUDES:
  LOW-DOSE t-PA (TISSUE-TYPE PLASMINOGEN ACTIVATOR—CathFlo Activase)

## Slide 42: CVAD INFECTION
MOST COMMON COMPLICATION
CAUSES:
  CONTAMINATED INFUSATE
  CONTAMINATION AT IV TUBING JUNCTIONS
  CONTAMINATION AT INSERTION SITE
  SYSTEMIC SEEDING FROM DISTANT SOURCE

## Slide 43: CVAD INFECTION
LOCAL OR SYSTEMIC
LOCAL INCLUDE:
  INSERTION OR EXIT-SITE INFECTIONS
  PORT OR RESERVOIR INFECTIONS
  TUNNEL INFECTIONS
SYMPTOMS:
INFLAMMATION WITH OUR WITHOUT PURULENT DRAINAGE
  LOCALIZED PAIN
  ERYTHEMA
  INDURATION
  TENDERNESS
PREVENTION:
  STRICT HAND WASHING
  ASEPTIC TECHNIQUE
  PROPER SKIN PREP

## Slide 44: CVAD INFECTION
SYSTEMIC INCLUDE:
  BACTEREMIA OR SEPTICEMIA
  SUPPURATIVE THROMBOPHLEBITIS
  ENDOCARDITIS OR ETASTATIC ABCESSES
IS RARE, BUT CAN BE LIFE-THREATENING
SYMPTOMS:
  FEVER
  CHILLS
  HYPOTENSION
  HYPERVENTILATION
  ALTERED MENTAL STATUS
  NONSPECIFIC GASTROINTESTINAL COMPLAINTS
    NAUSEA
    ABDOMINAL PAIN

## Slide 45: CVAD INFECTIONS
REMEMBER!!
IMMUNOSUPPRESSED CLIENTS MAY HAVE NO SYMPTOMS!!
DIAGNOSIS INCLUDES:
  BLOOD CULTURES
  SITE CULTURES
  CATHETER TIP CULTURES

## Slide 46: CVAD INFECTIONS
TREATMENT INCLUDES:
UNCOMPLICATED INSERTION/EXIT SITE INFECTIONS:
  FREQUENT SITE CARE
  10-14 DAYS OF ANTIBIOTICS
TUNNEL, TRACT, OR POCKET INFECTIONS
  USUALLY REQUIRE REMOVAL
  7-10 DAYS OF ANTIBIOTICS

## Slide 47: IV THERAPY IS COMING TO A HOME NEAR YOU!
CONVENIENCE
DECREASED EXPOSURE OF IMMUNOCOMPROMISED PATIENTS TO NOSOCOMIAL INFECTIONS
DECREASED ACUTE CARE COSTS